# General Description
The XMICRO-MEMORY is an XMICRO slave card providing 1MB of RAM and an optional relocatable 8KB EEPROM.
## Features
- 1MB SRAM fills all XMICRO bus memory address space
- 8kB EEPROM available to bus
## System Outline
Table 1: Card Memory Map / Address Range Function / $XFF Card ID Register (R)	Table 2: Card Configuration / Setting Function / JP1 Enable wait states for ROM accesses / JP2 Enable ROM / S1 ROM page selection / S2 ROM address selection
Table 3: ROM Address Examples / S2 Setting ROM Address Range / 0000000 $00000-$01FFF / 0000111 $0E000-$0FFFF / 0001000 $10000-$11FFF	Table 4: ROM Pages / S1 Setting Range on EEPROM / 00 $0000-$1FFF / 01 $2000-$3FFF / 10 $4000-$5FFF / 11 $6000-$7FFF

# RAM
The 1MB SRAM is “Main Memory” as descrived by the XMICRO bus specification. Bus read/write operations will default to this RAM, provided that IOSEL and INH are not asserted. When either IOSEL or INH are asserted, the XMICRO-MEMORY’s RAM is disabled.
# ROM
The ROM, when enabled, overrides the onboard RAM in the 8kB range specified using switch S2. When bus address bits A<19..13> match the setting on S2, the ROM is selected. See Table 3 for examples.
The 32kB EEPROM is divided into four pages of 8kB which are selected using switch S1. See Table 4 for page settings.
As the ROM operates significantly slower than the RAM, it is equipped with a wait state generator to meet timing requirements of high-speed bus masters.
# Onboard Registers
## Card ID Register ($XFF)
The Card ID Register contains the ID value $02 as assigned in XMICRO Bus specification Appendix A. This register is used by the system to determine card types and locations.